## Slide 1
THE ENGINE
Student Training Program
Team 2950 — The Devastators
6 Modules · 30 Quiz Questions · Prediction Engine Validated at 92%

## Slide 2
Training Modules
Module 1
Pattern Rules
17 rules + 10 meta-rules from 13 top teams
45 min
Module 2
Prediction Engine
Utility scoring, Bot Aborter, decision loop
60 min
Module 3
Design Intelligence
Kickoff pipeline, 254 analysis, Open Alliance
60 min
Module 4
Pathfinding
A* algorithm, navigation grids, dynamic obstacles
50 min
Module 5
Vision & YOLO
Camera pipeline, neural detection, field projection
55 min
Module 6
Sim & Testing
4 quality gates, AAA tests, maple-sim
55 min

## Slide 3
Module 1: Pattern Rules
17 rules + 10 meta-rules extracted from 13 championship teams across 10 seasons
Core Insight: The best FRC teams don't start from scratch. They apply proven design patterns.
Teams Studied: 254, 118, 1678, 6328, 4414, 1323, 2910, 1690, 3847, 2056, 1114, 973, 2826
Where to Find: constructicon/design-intelligence/CROSS_SEASON_PATTERNS.md

## Slide 4
The 17 Rules (Summary)
# | Rule | Confidence
1 | Swerve drive — no exceptions since 2022 | 100%
2 | Full-width intake — 'touch it, own it' | 95%
4 | Flywheel for throwing, elevator+wrist for placing | 90%
6 | Turret only when aiming while driving | 80%
7 | Climb mandatory when >15% of winning score | 95%
11 | Cycle speed above all else | 95%
16 | Dual pieces: one mechanism, shared motor | 85%
17 | Intake opposite scoring side | 90%

## Slide 5
10 Meta-Rules
# | Meta-Rule | Source
M1 | Simple beats complex when executed perfectly | 4414
M2 | Iteration speed > first design quality | 254
M3 | The team that drives more wins (50+ hrs practice) | 254
M6 | No pneumatics in 2026+ (20 motor slots) | 3847
M7 | Build multiple robots (AlphaBot / AM→FM) | 254, 3847
M8 | Backlash elimination for precision (Loctite 609) | 2056
M9 | Credit and learn from other teams publicly | 1323
M10 | Don't chase magic numbers — build in margins | 3847

## Slide 6
Module 2: Prediction Engine
How the robot decides what to do, every 0.5 seconds
Utility Scoring: Every action (SCORE, COLLECT, CLIMB, DEFEND) gets a score. Highest wins.
Bot Aborter: Abort if opponent arrives 0.75+ seconds before us.
Validated: ~92% accuracy against 2026 REBUILT game manual. Correctly predicted swerve + hopper + turret + flywheel + multi-rung climber + 115 lbs.

## Slide 7
Prediction Engine vs Reality
2026 REBUILT — Statbotics EPA
Team | Record | Total EPA | Auto | Teleop | Endgame
254 | 32-2 | 331.7 | 59.7 | 191.9 | 80.1
1323 | 34-0 | 313.5 | 53.1 | 192.2 | 68.2
118 | 63-5 | 158.3 | 27.9 | 94.5 | 35.9
Key insight: 254 and 1323 have nearly identical teleop EPA (~192) but 254 leads endgame by 12 points. The 2x gap vs 118 suggests turret + hopper + shoot-on-move is the differentiator.

## Slide 8
Module 4: Pathfinding
Navigation Grid: 164×82 cells (0.1m each) covering the FRC field
A* Algorithm: finds shortest path using f = g + h (actual + estimated cost)
8-directional movement: cardinal = 1.0, diagonal = √2 cost
Dynamic obstacles: opponent bounding boxes stamped every 20ms cycle
Re-planning: every 0.5s, on Bot Aborter trigger, or if robot drifts >0.3m

## Slide 9
Module 5: Vision & YOLO
Wave Robotics YOLOv11-nano: 2.59M params, 30+ fps on Limelight 4 Hailo
Pipeline: camera → YOLO inference → NMS → confidence filter → field projection
3-frame persistence prevents false positives (must appear 3 consecutive frames)
Dual cameras: Limelight 1 for AprilTag pose, Limelight 2 for game piece detection
HSV color fallback activates automatically if YOLO model fails to load

## Slide 10
Module 6: Simulation & Testing
4 quality gates: Spotless (format) + SpotBugs (bugs) + JUnit (tests) + JaCoCo (coverage)
246+ tests following Arrange-Act-Assert pattern, all HAL-free
maple-sim provides swerve physics — test autonomous without a robot
AdvantageScope connects to localhost:3300 for live field visualization
Known bug: maple-sim motor forces inverted for REV hardware (kinematic bypass active)

## Slide 11
Ready to Build
17 rules · 10 meta-rules · 13 tracked teams · 10 seasons of data
Prediction engine validated at ~92% accuracy against REBUILT
Your swerve code is the foundation. The Engine is what we built on top.
Team 2950 — The Devastators